## Slide 1: EV3 Classroom: Proportional Control
By Sanjay and Arvind Seshan

## Slide 2: Lesson Objectives
Learn what proportional control means and why to use it
Learn to apply proportional control to the ultrasonic sensors
Prerequisites: Operator Blocks (Math Blocks), Ultrasonic Sensor

## Slide 3: Learn and Discuss Proportional Control
Let’s start with a game
Imagine that you blindfold one teammate. He or She has to get across the room as quickly as they can and stop exactly on a line drawn on the ground
The rest of the team has to give the commands.
When your teammate is far away, the blindfolded person must move fast and take big steps. But as he gets closer to the line, if he keeps running, he will overshoot. So, you have to tell the blindfolded teammate to go slower and take smaller steps.
You have to program the robot in the same way!

## Slide 4: What Proportional Control Looks Like
The Pseudocode for every proportional control program consists of two stages:
  Computing an error  how far is the robot from a target
  Making a correction  make the robot take an action that is proportional to the error (this is why it is called proportional control). You must multiply the error by a scaling factor to determine the correction.
Compute Error
Make Correction

## Slide 5: Challenge
To learn how to use proportional control, create a Robot Follower program
  Use proportional control with the ultrasonic sensor to get the robot to stay 15cm away from the human at all times (even when the human moves)
Objective | Error | Correction
Get to a target distance from human | How many cm from target location (current_distance – target_distance) | Move faster based on distance

## Slide 6: Challenge
Compute Error | 
How many cm from target location (current_distance – target_distance) | 
Compute/Apply Correction | 
Multiply by scaling factor and adjust speed based on distance | 
error
error

## Slide 7: Putting It All Together: Ultrasonic Robot Follower
Loop so that the robot keeps applying an updated correction based on the ultrasonic reading
Compute the error, multiply by the scaling factor, and apply a correction

## Slide 8: Discussion Guide
What does proportional control mean? Ans. Moving more or less based on how far the robot is from the target distance
What do all proportional control code have in common? Ans. Computing an error and making a correction

## Slide 9: Credits
  This tutorial was created by Sanjay Seshan and Arvind Seshan
  More lessons at www.ev3lessons.com
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.